## Slide 1: ALARM FATIGUE IN NICU Understanding the Risks and Solutions to Improve Patient Safety
Hamideh nikzad
Nidcap certified
1404
مرکز آموزشی درمانی الزهرا -تبریز

## Slide 2: Auditory intervention
The uterine environment protects the developing fetus from loud and high frequency sounds
But in the NICU this protection is lost and harsh clinical environment is replaced

## Slide 3
دسی بل | میزان صداهای ثبت شده در NICU
45 تا60 | صداهای پس زمینه ای محیط
60 | صحبت کردن معمولی پیرامون بستر نوزاد
65 تا 70 | آلارم پمپ انفوزیون
86 | پالس اکسی متری
75 | گریه نوزاد
80 | زنگ تلفن
80 تا 90 | ضربه انگشتان به انکوباتور
62 تا 87 | حباب درون لوله های ونتیلاتور
100 تا 135 | بستن درهای انکوباتور

## Slide 4: Effect of noise on preterm infants
Crying
Behavioral disturbances
Autonomic changes
Language or auditory disorders
Apnea
Sleep deprivation
Tachycardia
ICH
Hypoxia

## Slide 5: Auditory interventions consist
Sound levels should not exceed an average of 45 db.
Quiet conversations at baby’s bed
Avoiding use of headphones/ mobile phones
Handling doors and carts gently
Silencing alarms promptly
Maternal live singing (is beneficial)

## Slide 6: What is Alarm Fatigue?
When caregivers are exposed to many alarms
that they become desensitized
slower to respond
or start ignoring alarms

## Slide 7: Effects on Nurses
Increased stress and anxiety
Decreased job satisfaction
Burnout and compassion fatigue
Impaired focus and teamwork

## Slide 8: Effects on Patients and Families
Interrupted sleep and rest
Increased stress for infants and
families
Delayed response to true
emergencies
Potential for adverse outcomes

## Slide 9: Why Focus on the NICU?
Neonates are high‐risk
physiological changes rapid
monitoring essential
Alarm fatigue undermines patient safety.

## Slide 10: Magnitude of the Problem in NICU
In a study in a NICU before intervention, only 31% of alarms were “true alarms” and 69% non‐actionable; after an Alarm Management Program, true alarms rose to 57% and non‐actionable fell to 43%.

## Slide 11
Studies: Up to 85–95% of alarms are non-actionable in NICUs
Average: >150 alarms per infant per day

## Slide 12: Contributing Factors
Sensitive alarm limits
Lack of standardization
Poor alarm customization
Equipment malfunction or artifact
High patient acuity and workload

## Slide 13: Causes of Alarm Fatigue in the NICU
High frequency of false or non-actionable alarms
Overlapping alarms from multiple devices
Sensitivity settings not tailored to individual patients
Environmental noise
Staffing constraints and workload pressure

## Slide 14
Cause | Description | NICU Examples
High Frequency of Alarms | Too many alarms in a short time; staff exposed to constant alerts | Multiple monitors per patient; 80–90% non-actionable alarms
Low Specificity / Poor Clinical Relevance | Alarms triggered by minor or irrelevant events | Baby movement; sensor displacement; temporary SpO₂ drops
Inadequate Alarm Settings | Default thresholds too sensitive; lack of patient-specific adjustments | Pulse oximeter alarms set to narrow range for all neonates
Environmental & Workflow Factors | Noise, overlapping alarms, poor escalation systems | Open-bay NICU with simultaneous alarms; high ambient noise
Staff-Related Factors | Fatigue, stress, high workload reduce responsiveness | Long shifts; high nurse-to-patient ratio; delayed alarm response
Equipment Factors | Malfunctioning or inconsistent devices; confusing alarm sounds | Old monitors producing false alarms; multiple tones hard to distinguish

## Slide 15
Delayed or missed responses to critical alarms
Increased risk of adverse events

## Slide 16: Common Types of Alarms in the NICU
Cardiorespiratory monitor alarms (heart rate, apnea, oxygen saturation)
Ventilator alarms
Infusion pump alarms
Crib or incubator
Humidifiers

## Slide 17: Strategies to Reduce Alarm Fatigue
Adjusting alarm thresholds and delays appropriate for neonatal population.
Education and training of staff
Device/Monitor optimization and maintenance
Multidisciplinary team & alarm management program (AMP)
Reduce background noise

## Slide 18: Technology Solutions
Smart alarms and integrated systems
Visual or silent alerts
Central monitoring stations

## Slide 19: Single-family room (SFR) NICUs are better than open-bay NICUs
Advantages of Single-Family Rooms (SFRs):
Lower noise levels
Improved alarm clarity
Reduced sensory overload
Better customization

## Slide 20: But caveats are:
Nurses may not hear alarms from other rooms as easily, so systems must ensure alarms are transmitted effectively (through pagers, smartphones, or centralized monitoring).
Alarm escalation design is critical — without a good secondary notification system, single rooms might increase response time to alarms.

## Slide 21: Cautions
SFRs require strong alarm communication systems (mobile devices, central monitoring)
Inadequate design could cause delayed responses if alarms aren’t effectively transmitted.

## Slide 22
Single-family room designs can
significantly mitigate alarm fatigue and enhance patient safety.

## Slide 23: Role of Nurses
Report malfunctioning equipment
Assess alarm appropriateness per patient
Advocate for policy changes
Participate in education and audits

## Slide 24: Summary
Alarm fatigue threatens safety and well-being
Most alarms are non-actionable
Customization, education, and teamwork reduce fatigue
Nurses are key to improvement

## Slide 25
Thanks for your attention